## Slide 1: Use of function generator and oscilloscope

## Slide 2: Digital oscilloscope
Components of a DSO
1) analog vertical input amplifiers
2) ADC
3) Writes to memory,
4) a time base which features a triggering and clock drive
circuits for waveform display and reconstruction, the LED or LCD display, and
power supply.
Digital oscilloscopes periodically samples a time varying analog signal ( satisfies Nyquist criterion)
and stores in the waveform memory the signal’s values in correlation with time.

## Slide 3: Advantages of a DSO
Since the data is stored, it can be retrieved for viewing and analysis later
Easily do signal averaging to reduce noise
Can get a single shot event ( good for non-repetitive events).

## Slide 4: Triggering
How does the oscilloscope know when to start
taking data ?
This is done by setting a trigger. This is usually a voltage level.
Triggering modes AUTO and NORMAL. However, NORMAL is not the normally used mode of triggering.
The normally used mode of triggering is AUTO

## Slide 5: Triggering
In auto mode, the scope will trigger whenever a trigger level is met. The trigger can just be a voltage level or a rising or falling edge of a signal or trigger from ch 1 when u r on ch2.

## Slide 6
Examples of Positive and Negative Slope Triggering

## Slide 7
If the trigger condition is not met the oscilloscope will generate its own triggers which is not synchronous with the signal under test.
A simple sine wave can look like this if not triggered properly

## Slide 8
Auto mode is also useful to see if there is a dc level offset of the signal
Auto mode is useful to see what trigger level to
set when the signal is noisy

## Slide 9: (External trigger ) Normal mode
You can decide which part of the waveform u
can trigger. The trigger can be synchronous with
the signal. It is very useful for single shot operation

## Slide 10: Arbitary Function generator (AFG)
Advantages of synthesised waveforms
Almost the only way to have very low harmonic
content in a sine way.
Generate any waveform in software- difficult or
impossible in hardware.
How does the choice of impedance value influence
the waveform?
Set limits on amplitude to protect DUT